## Slide 1: Power from Nuclear Transmutation (Fission and Fusion)
The Diablo Canyon NPPT produced CO2-free electricity at 2¢/kwh, half the state’s (CA) average cost.
Notes: Georgia Power announced this week that the 1,114-megawatt (MW) Unit 4 nuclear power reactor at Plant Vogtle near Waynesboro, Georgia, entered into commercial operation after connecting to the power grid in March 2024. The commercial start of Unit 4 completes the 11-year expansion project at Plant Vogtle. No nuclear reactors are under construction now in the United States.
Vogtle Unit 3 began commercial operation in July 2023. The plant’s first two reactors, with a combined 2,430 MW of nameplate capacity, began operations in 1987 and 1989. The two new reactors bring Plant Vogtle’s total generating capacity to nearly 5 gigawatts (GW), surpassing the 4,210-MW Palo Verde plant in Arizona and making Vogtle’s four units the largest nuclear power plant in the United States.

## Slide 2: Agenda
Nuclear stability & particle radiation Potential biological hazards
Energy Generation from Nuclear Fission U.S./World trends, Nuclear fuel resources (U.S.),
  Fission chain reaction and reactor control,
  Reactor types, Fuel cycles, radioactive waste & storage.
New Nukes: Advanced Nuclear Energy Technologies
  Small modular plants, Advanced (Gen IV) reactors, U & Th breeder reactors, subcritical reactors, Closed fuel cycle, Non-fission applications: Radioisotope Thermoelectric Generators (RTG)
Energy from nuclear fusion reactions Fusion energetics, critical Principles of magnetic and inertial confinement
Strategic Issues for Nuclear Power
Sustainability, reliability, scalability, safety, eco-footprint, cost

## Slide 3: U.S./World Trends in Nuclear Energy Production
Steady increase of nuclear power output over 30y. Efficiency e ↗ Now: e ≧ 90%  equivalent: 24 quads of oil. NPP lifetime 40a  > 60a
World 2023 (US): 440 (92) reactors; 400 (100) GW, 2.5 PWh  Modernize !
World Trend >53 new NPPt 2050: 600GW ?
US(since 2012): +3 -6 > 20 planned (?)
license app US potential:
1.Extend plant lifetime,
2.N new reactors/a (@ $(3-4)B/GWe  (5-10)¢/kWh)
Several new companies  SMR, Na-cooled Microreactors
Fusion Demos
GW
Most recent
GW
Notes: With a total installed capacity of about 97 GW, the largest commercial nuclear generating fleet of any country is located in the United States. The fleet of operating nuclear power reactors accounted for nearly 19% of domestic electricity production in 2023, making nuclear the second-largest source of U.S. electricity generation after natural gas, which accounted for 43% of electricity generation in the United States last year.
***In 2019 globally 5.5 GW of additional nuclear capacity were connected to the grid and 9.4 GW were permanently shut down, bringing global capacity to 443 GW. New projects were launched (about 5.2 GW), and refurbishments are under way in many countries to ensure the long-term operations of the existing fleet. Nevertheless, while the existing nuclear fleet remains the world’s second most important low-carbon source of electricity, new nuclear construction is not on track with the SDS. According to current trends, nuclear capacity in 2040 will amount to 455 GW – well below the SDS level of 601 GW. Additional lifetime extensions and a doubling of the annual rate of capacity additions are therefore required.
Georgia Power Co. announced Monday that Unit 3 at Plant Vogtle, southeast of Augusta, has completed testing and is now in commercial operation, seven years late and $17 billion over budget. First new reactor built from scratch.
At its full output of 1,100 megawatts of electricity, Unit 3 can power 500,000 homes and businesses. A number of other utilities in Georgia, Florida and Alabama are receiving the electricity, in addition to the 2.7 million customers of Southern Co. subsidiary Georgia Power.
South Carolina Electric & Gas Co. and state-owned utility Santee Cooper spent more than $9 billion before abandoning construction on the reactors at the V.C. Summer Nuclear Station near Columbia last year. State and federal authorities are probing the failure, and irate customers and shareholders have filed lawsuits.

## Slide 4: U.S. Uranium Resources/Used Fuel Elements
1GWe nuclear reactor requires yearly core load of (17.5-20) t low-enriched uranium U3O8 (3.5 - 5)% U-235, > 95% U-238
Used fuel elements in NP stations is U enriched in U-235. Used fuel elements: < 3 % U-235, > 95% U-238= fertile fuel for breeding.
Future small modular ppt, U, Th breeder reactors, Nuclear Magnetic Confinement fusion demos.

## Slide 5: Basic Nuclear Properties
12C =stable isotope >>>14C or C-14<<< =radioactive isotope
Atom of element Z: Z negatively charged electrons orbit around a Z-times positively charged, small nucleus in center of atom. Nucleus= (Z protons, N neutrons), mass number A = N+Z
Nuclear radii range from RNucleus ≈(1-10)·10-15m. (1 fm= 10-15m)
Nuclear radius RNucleus « RAtom atomic radius ( 1Å=10-10 m)
Nuclear mass unit: u := 931.5 MeV/c2
mproton =1.00728 u, mneutron= 1.00866 u
mneutron > mproton
Classical Model of Atom
Isotope Terminology
Mean Specific Nuclear Binding Energy B/A
Fe, Ni
Nuclear mass mA < N·mneutron + Z·mproton  Dm·c2 = binding energy B >0.

## Slide 6: Basic Energetics: Nuclear Rearrangement Energies
Einstein: equivalence mass = energy E = M·c2
Mass M(N,Z) < N·Mn + Z·Mp  DM ∝ B(A=N+Z)
Energy release in fission A2A/2
Fe Ni
Energy of fusion: B=DM·c2 is released
236U
Fission of 235,238U from g.s. is not spontaneous  Activation energy = Fission Barrier
Pass via n-capture 235U+n236U*

## Slide 7: Fuel Energy Density
From P. W. Huber & M. P. Mills, “The Bottomless Well,” Basic Books, New York, 2005
From Wikipedia, Nov. 2012
Nuclear fuel has highest known material energy density (~107)  potentially lowest environmental impact (“footprint”)
Energy Density (MJ/kg)
108
107
100
Fission Reactions

## Slide 8: Energy Release in nth-Induced Fission
Converts 0.1% of the mass  energies of fragments+n
Thermal energy/heat
1g 236U/day = 1MW >106 x chemical energies
Eff = 168 MeV En tot = 5 MeV Eg = 7 MeV FF b-decay = _27 MeV Qtotal = 207 MeV
236U*
fission fragment
fission fragment
n
n
n
highly unstable
Additional fuels: 239Pu Fertile actinides 223Th, 238U can be made into nuclear fuel by neutron irradiation (“breeding”)
thermal E= (3/2)kBT, kBT=25meV
Fission fragments have a distribution

## Slide 9: b-Delayed Neutrons
87% of fission energy (≈200 MeV) promptly in fission ≤ 10-14 s 13% emitted in b-decays of fission fragments, range of life times  delayed emission of b+, b-, ne, g, n
0.65% of neutrons from 236U fission are delayed (occur after fission)  = Essential for sustaining chain rxn + control function
b-delayed neutron <Dt> ≈ 80 s
k<1  keff≈1 Effective neutron multiplication factor, but not all “survive”
Most have “wrong” energy for 235U chain rxn
Fission Fragment
86Kr+n
87Kr
87Br
b- (2%)
b-
b-
87Rb
87Sr
b- (98%)
(55.6 s)
(76 m)
(5·1010a)
Example
Energy
“Ignition” possible?  self-sustaining chain reaction

## Slide 10: Self-Sustaining Fission Chain Reaction
Neutron multiplication through fission: k=2.4, minus losses (capture, leaking, escape,..)  effective k < 1. One n used in each fission  effective multiplication k-1
Leo Szilard 1938
k >1: avalanche of n t = time between generations (t ~ 40ms in critical reactors t ~ ns in explosive devices)
Reactor Control: delayed n’s
keff≈1 e.g.,keff=1.03
Most fission neutrons are lost or not useful for further fission. Fission fragments = “reactor poison”  keff < 1 stops chain reaction!
Characteristic time period
Self-Sustaining Chain Reaction

## Slide 11: Fission and n-Capture Probabilities (“Cross Sections”)
Neutron Kinetic Energy (eV)
Neutron Capture and Fission Cross Sections (b=10-24cm2)
235U+n
238U+n
n capture
n capture
fission
Fast-neutron fission
natU: 99.3% 238U, 0.7% 235U
Fission cross sections  typically small, 238U: sf ~ 1 b for En > 1 MeV ≈ 0 b for En < 1 eV dominating: scattering (~8 b) + capture
235U: sf ~ 1-2 b for En > 1 MeV ~ 103 b for En < 1 eV large!! dominating: (n, f) fission
Observed natU fission is due to (0.7%) 235U
isotopically enrich 235U, > 4% -20% for higher efficiency ( output fission energy/input neutron energy)
Central Problem: Ignition of a self-sustaining fission reaction.  Moderate & recycle fission neutrons!
Quantum Mech. 239U “resonance”
Slowing-down (moderation) of fission n‘s by elastic n scattering on light moderator nuclei (H, C,…)
“cross section” ∝ Probability/Nucleus
99.3% nat
0.7% nat
Slow neutrons  large sf!

## Slide 12: Neutron Energy Moderation
Fast Neutrons from U-236 Fission
Fission neutrons too energetic,  “thermalize” to maximize sn,fiss for 235U !  multiple elastic scattering (“moderation”) moderator: small scapt !
A=238
A=65
A=12
A=1
moderator
n-reflector
U
U
U
Slow down for capture !
H, D are best moderators
H2O moderator
H can capture neutrons (k < 1 !): H+nth  D+2.2 MeV
Need:2 MeV  0.025 eV/2MeV (= 10-8) Must “miss” 238U capture resonances (2eV < En <10keV)
H2O, D2O, Be, C(graphite), prevent n leakage
Needed: moderator and fuel coolant
Control rods (Cd,..) capture n’s  keff ≈1
Cd Control rods

## Slide 13: Reactor Control and Safety
“Reactivity dr/dT “;  = (keff -1)/keff Reduce by n absorbers Cd, B (control rods, moderator) Automatic: fission products= “reactor poisons“
In BWR/PWR Doppler Effect: broadening of resonance and n spectrum leads to increased n-capture by 238U  dr/dT < 0
Density Effect: hot moderator expands, lower density  longer mean free path, less moderating efficiency  dr/dT < 0
Dilatation Effect: hot moderator delays slowing down  dr/dT < 0
U
U
U
Cd Control Rods
Temperature dependent reactivity coefficient dr/dT<0  Negative reactivity desirable (self-regulating).
dr/dT = -(0.5-1)x10-4/0C PWR
dr/dT = - 1x10-3/0C Breeder, EA

## Slide 14: Principle Boiling Water Reactor

## Slide 15: Boiling Water Reactor/Fuel Assembly
Reactor core with fuel.
Water (moderator/coolant) streaming through core.
Separators dry steam-from water droplets, before it enters steam line.
Steam line to main turbine/ generator producing electricity.
Centrifuge Array
Notes: The unused steam is exhausted to the condenser, where it is condensed into water. The resulting water is pumped out of the condenser with a series of pumps, reheated, and pumped back to the reactor vessel. The reactor's core contains fuel assemblies that are cooled by water circulated using electrically powered pumps. These pumps and other operating systems in the plant receive their power from the electrical grid. If offsite power is lost, emergency cooling water is supplied by other pumps, which can be powered by onsite diesel generators. Other safety systems, such as the containment cooling system, also need electric power. BWRs contain between 370-800 fuel assemblies.

## Slide 16: Pressurized-Water Reactor (PWR)
Reactor core, contains fuel creates heat.
Pressurized water primary coolant loop to steam generator.
Steam generator vaporizes water in a secondary loop.
Steam line to the main turbine/ generator producing electricity.
Notes: The unused steam is exhausted to the condenser, where it is condensed into water. The resulting water is pumped out of the condenser with a series of pumps, reheated, and pumped back to the steam generator. The reactor's core contains fuel assemblies that are cooled by water circulated using electrically powered pumps. These pumps and other operating systems in the plant receive their power from the electrical grid. If offsite power is lost, emergency cooling water is supplied by other pumps, which can be powered by onsite diesel generators. Other safety systems, such as the containment cooling system, also need electric power. PWRs contain between 150-200 fuel assemblies.

## Slide 17: Conventional Gen-II Nuclear BW Power Plant 1-2GW
Passive safety: Pressure reactor vessel ~1’ thick steel, pressure tubes,
Reactor containment building with several 3-5-feet-thick concrete walls, concrete + water shielding on top of reactor vessel, gravitation replaces mechanical pumps.
Fail-safe operation
Negative Reactivity
Negative feedback loops:
Reaction subsides when
coolant gets too hot or
disappears (less dense,
less moderation)
fuel gets too hot
(n capture increases)
control rods are not
moved out
2-3 B$/1GWe NPP
Fuel Elements
Nuclear Island
Generator Island

## Slide 18: PWR Primary and Secondary Cooling Systems
Pressurizer tower 13.5m 4.4m Ø
Generator Island
Nuclear Island

## Slide 19: Nuclear Fuel Storage & Transport
Progress Energy

## Slide 20: Uranium and Thorium Fuel Cycles
US: Once-through
Closed fuel cycle with reprocessing (France, Japan, Russia, India, ...)
Geological Depository in Carlsbad/NM
Worldwide: 5 geological depositories in operation (US: 1)
Yucca Mountain
Stopped in 2010, temporarily?
35 tons U fuel
Uranium Fuel Conversion
Permanent storage of high-level waste already paid for by consumers
¢0.1/kWh.
“Spent fuel” still contains 97% of nuclear energy (235,238U, 239,240Pu) + FF & MA
 A, A+1,..
Thorium Fuel Conversion
Notes: A type of nuclear reactor fuel (often called "MOX") that contains plutonium oxide mixed with either natural or depleted uranium oxide, in ceramic pellet form. (This differs from conventional nuclear fuel, which is made of pure uranium oxide.) Using plutonium reduces the amount of highly enriched uranium needed to produce a controlled reaction in commercial light-water reactors. However, plutonium exists only in trace amounts in nature and, therefore, must be produced by neutron irradiation of uranium-238 or obtained from other manufactured sources. As directed by Congress, the NRC regulates the fabrication of MOX fuel by DOE, a program that is intended to dispose of plutonium from international nuclear disarmament agreements. For further detail, see the Backgrounder on Mixed Oxide Fuel and Frequently Asked Questions About Mixed Oxide Fuel.

## Slide 21: Fuel Cycle: Fuel Enrichment
Paducah/KY Separation Plant
plant control room
Cylinders spin at 1.5km/s surface velocity  centrifugal forces produce different sedimentation rates

## Slide 22: Gas Diffusion Isotope Enrichment
Preferred technology: Gaseous diffusion of UF6 (19F mono-isotopic)
Laser ionization possible, economics
1.5% mass difference
US: NPP (7TWh/a output) needs 250 GWh/a for enrichment
Intermediate enrichment ~20% needed for research & radio-pharma reactors
NPP (7TWh/a output) needs ≈ 6 GWh/a for 0.7  6% 235U

## Slide 23: Yucca Mountain (NV) Depository
Spent-fuel canisters, sealed in special casks, are shipped to the site by truck or train.
Shipping casks are removed, inner tube with fuel elements is placed in a steel, multilayered storage container.
Automated system sends and manages storage containers in underground tunnels.
Containers stored on their side along the tunnels.
Retrievable for later use (or not)
16 countries have geological depositories
Notes: Deep geological disposal is the preferred option for nuclear waste management in most countries, including Argentina, Australia, Belgium, Canada, Czech Republic, Finland, France, Japan, the Netherlands, Republic of Korea, Russia, Spain, Sweden, Switzerland, the UK, and the USA.

## Slide 24: Radioactive Waste: Power Reactors/Weapons Stewardship
High-level waste depository for geological times  Yucca Mtns/NV ? Radio-chemical reprocessing
Very-long-lived 99Tc, 129I >could< dissolve in groundwater and move through ecosystem  disposal strategies for isolation.
Better: reprocessing, transmutation/incineration of 99Tc, 129I, Np
1 Sv (Sievert) = 100 rem, biolog. equivalent to 1J/kg X-rays Radiotoxicity: R(Sv)=(Dose in Sv/decay), Activity/kg
R3: fast-n reactors (“incinerators”) +reprocessing
FF
Nat Uranium Ore
R3

## Slide 25: Agenda
Nuclear stability & particle radiation Potential biological hazards
Energy Generation from Nuclear Fission U.S./World trends, Nuclear fuel resources (U.S.),
  Fission chain reaction and reactor control,
  Reactor types, Fuel cycles, radioactive waste & storage.
New Nukes: Advanced Nuclear Energy Technologies
  Small modular plants, Advanced (Gen IV) reactors, U & Th breeder reactors, subcritical reactors, Closed fuel cycle, Non-fission applications: Radioisotope Thermoelectric Generators (RTG)
Energy from nuclear fusion reactions Fusion energetics, critical Principles of magnetic and inertial confinement
Strategic Issues for Nuclear Power
Sustainability, reliability, scalability, safety, eco-footprint, cost

## Slide 26: U.S. Electricity Generation
Forecast:
Total electricity demand: 3.8 1015 Wh/a (2011)  5.1 1015 Wh/a (2040),  D= 1.1 %/a, accounting for eff gains.
Recent rapid decline of natural gas prices  projected mean delivered electricity prices 9.9 c/kWh  9.2 c/kWh (2015).
Retire 7GW Gen II in the next 10 years (?)
PWh
+ Hydro
Projected scenario BAU is workable but increases GHG output.

## Slide 27: U.S. 2020 Nuclear Statistics (EIA)

## Slide 28: Agenda
Energy Generation from Nuclear Fission
  Nuclear binding/rearrangement energies
  Fission chain reaction and reactor control
  Reactor types, nuclear fuels, fuel cycle
Advanced(Gen IV) Nuclear Energy Technologies
  Small modular reactors, MSR-LFTR, Th breeder, ADR
  Closed fuel cycle
  Reactor inventory and trends in nuclear fission power
Strategic Issues for Nuclear Power
  Safety, eco-footprint, cost, scalability
  Proliferation safety
  Biological effects of radiation
Energy Generation from Nuclear Fusion
  Principles of energy conversion
  Tokamak scheme